## Slide 1: Yocto Tutorial Beginner
Yaron Daniel

## Slide 2: Syllabus
Introduction
  Embedded system
  Embedded Linux
  Linux distribution build platforms
  Petalinux compare Yocto
  OpenEmbedded and Yocto
Yocto
    Install and Build image
    Bitbake
    Poky
    Layers
    Bblayers.conf
    Local.conf
    Build system
    Artifacts
    Packages
    Recipes
    Recipes build task
    Assignment and Basic assignment
    Variables

## Slide 3: Syllabus - continue
  Yocto
    Appends files
    images
    Classes
    Kernel configuration
    Uboot configuration
    SDK
    Practice
  Yocto with Xilinx BSP layers
    Xilinx Layers
    Configuration
    BSP Xilinx Configuration
  Appendix – Rafael shield distro

## Slide 4: Embedded Systems - Overview
Embedded system is a combination of a computer hardware and software designed for a specific function
The systems can be programmable or have a fixed functionality
Example include :
  Automotive : modern cars commonly consist of many computers ,design to perform different tasks within vehicle . Such as adaptive cruise control ,forward collision warning , navigation system etc..
  Mobiles phones : these consist of many embedded systems including GUI software and hardware , operating systems , cameras , microphone etc..
  Industrial machines : sensors , automation system that perform specific monitoring and control function .
  Medical equipment : sensors , control mechanism , complex OS for GUI , CT scan , X-ray , MRI , etc..

## Slide 5: Embedded Systems – Characteristics
Consist hardware , software and firmware
  Basic Hardware : processor, power supply, memory, flash,communication port.
  Firmware : implement of FPGA
  Software : embedded OS , application task.
Can be embedded in a large system to perform a specific function , as they are built for specialized task within the system.
Can be microprocessor or microcontroller and compute power.
Real time : require to perform their function under a time constraint to keep the larger system functioning properly (usually baremetal , linux by default is not real-time.)

## Slide 6: Embedded Linux - Overview
Embedded linux refers to the use of the Linux Kernel , along with a comprehensive set of libraries and utilities, within embedded system or devices.
These systems, which are designed for specific functions, often feature constraints on resource like processing power, memory and energy consumption.
Linux due to its open-source nature, flexibility and robustness has become a popular choice for these systems.

## Slide 7: Embedded Linux
A linux distribution or distro is an operating system made up of the linux kernel along with a package management system and various libraries , drivers and utilities .
In the context of the Embedded linux, a distribution is often stripped down and customized to fit the needs of the specific embedded system it’s intended to run on.
There are several linux distribution platform specifically designed for embedded systems, such as OpenWrt, Yocto and buildroot.

## Slide 8: Linux distribution platforms
Buildroot : Based on set of Makefiles and patches that simplifies and automates the process of building a complete and bootable linux environment while using cross-compilation to allow building for multiple target platforms on a single linux based development system.
  Easy to use
  Limited configuration settings
  Requires full image rebuild
OpenWrt : Is an open-source project for embedded based on linux , used on embedded devices to route network traffic . All the components have been optimized to be small enough to fit into the limited storage and memory available in home routers.
  Focused on networking gear (routers)
  Packages based updated
Yocto : Yocto project is an open source project imitated by linux foundation . It provide a set of tools and metadata that enable developers to build custom linux distributions for embedded systems.
PetaLinux : Is a development enviorment by Xilinx , a leading provider of FPGA and SOC solution . It designed to streamline the development process for embedded linux system on Xilinx devices . MPSOC and Zynq SOC.

## Slide 9: PetaLinux compare Yocto Overview
PetaLinux Advantages
  Specialized for Xilinx hardware – specifically tailored for Xilinx FPGA and SOC
  Streamlined workflow – more integrated and streamlined for Xilinx development to Yocto – can reduce development time.
  Xilinx support
  Pre-built components – configuration optimized for Xilinx devices.
PetaLinux disadvantages
  Vendor Xilinx – lock – not intended for other targets
  Limited flexibility – lack of the flexibility and customization options provided by Yocto
  Dependency on Xilinx tools – heavily relies on Xilinx development tools which can introduce dependencies and constraints in the development process .

## Slide 10: PetaLinux compare Yocto Overview
Yocto Advantages
  Platform independence – Yocto project can be used to build custom linux for a wide range of embedded .
  Highly customization – Yocto offers extensive flexibility and customization options through its layer based architecture , allowing developers to tailor linux distribution to specific reequipment .
  Large community support.
Yocto disadvantages
  Learning curve – Yocto project has a steep learning curve , especially for beginner due to its complexity and extensive feature set. Getting started and mastering the workflow may require time and effort.
  Configuration overhead – Yocto require more configuration and setup compared to petalinux. (can be less if we used Xilinx layers for Yocto)
  Potential integration failures.
Summary: the choice between Petalinux and Yocto project depending on factors of hardware (Xilinx or not) , development preferences , customizations needs and resources (time) .

## Slide 11: OpenEmbedded and Yocto
OpenEmbedded is the underlying build framework , while Yocto project builds upon it to provide a comprehensive set of tools , documents,and best practices for embedded linux development .
Developers often use the Yocto project to create custom linux distro for their embedded systems , leveraging both OpenEmbedded capabilities and additional features provide Yocto.

## Slide 12: Yocto

## Slide 13
Install and build image
Download page:
- https://docs.yoctoproject.org/4.0.18/brief-yoctoprojectqs/index.html (kirksotne version)
- Include step by step install (quick build) and system requirement according to branch version .
Releases tables: https://wiki.yoctoproject.org/wiki/Releases
Include data for supported versions and status
Notes: 13

## Slide 14: Install and build image
Steps:
sudo mkdir -p /YoctoStudent
Sudo chown -R ubuntu /YoctoStudent
cd /YoctoStudent
Install Packages:
  sudo apt install gawk wget git diffstat unzip texinfo gcc build-essential chrpath socat cpio python3 python3-pip python3-pexpect xz-utils debianutils iputils-ping python3-git python3-jinja2 libegl1-mesa libsdl1.2-dev python3-subunit mesa-common-dev zstd liblz4-tool file locales
sudo locale-gen en_US.UTF-8
git clone git://git.yoctoproject.org/poky
cd poky
git checkout -t origin/kirkstone -b my-kirkstone
. oe-init-build-env
export LC_ALL=C # for every terminal add this line to ~/.bashrc
bitbake core-image-minimal
Show on terminal (without run bitbake build – just check that bitbake is working)

## Slide 15: Bitbake
The task executor and scheduler used by the OpenEmbedded build system to build images.
It reads metadata , recipes and executes tasks defined in those files to build software packages and create images.
Build command:
  Bitbake <image_name>
  Bitbake <recipe_name>
  Bitbake <recipe_name> -c <command>
    Flag c is identify task to do with the recipe.
Clean command:
Bitbake <recipe_name> -c clean
  Remove all output for a target : unpack,configure,install,compile,package
Bitbake <recipe_name> -c cleansstate
  Remove shared state , and the clean task.
Bitbake <recipe_name> -c cleanall
  Remove shared-state task and download source

## Slide 16: Poky - Overview
Reference embedded distribution and a reference test configuration.
Poky provide the following :
  A base-level functional distro used to illustrate to customize a distribution.
  test the Yocto components
  Includes : Bitbake ,tools,devtool,scripts OpenEmbedded-core,documentation and source of information.
  Layers:
    meta - This is the core layer , It includes the fundamental recipes, classes, and configurations needed to build a basic Linux system
    meta-poky - These layers contain additional metadata , includes additional configuration and policy settings,
    Meta-yocto-bsp - provides support for reference hardware platforms
  Show link :
  poky: Poky is a reference distribution of the Yocto Project®.

## Slide 17: Poky User Configuration – Scheme

## Slide 18: Layer Overview
A collection of related recipes . (such as graphic,multimedia,etc..)
Layer allow you to consolidate relate metadata to customize your build. (debug,oper,..etc)
Layer allow isolate information used when building for multiple architectures (projects).
Layer are hierarchical in their ability to override previous specifications.(bbappend,inherit bbclass)
You can include any number of available layers from the Yocto project and customize the build by add our layers (configure conf file,machine,device-tree ,etc..)
In this tutorial we will demonstrate and build our own layer.

## Slide 19: Layer - bblayers.conf
bblayers.conf is a configuration file used by the build system.
In this file the set of layers are defined ,should be included in a build.
The bblayers.conf file specifies the location of each layer on the local file system.
This file actually manage the layers for build

## Slide 20: Layers practical
Show on terminal commands:
  Help : bitbake-layers –h
  Show layers : bitbake-layers show-layers
  Create layer : bitbake-layers create-layer <path/to/layer>
  Add layer : bitbake-layers add-layer <path/to/layer>
Example:
  Bitbake-layers create-layer ~/YoctoStudent
  Bitbake-layers add-layer ~/YoctoStudent (from build dir)
  Bitbake core-image-minimal

## Slide 21: User Configuration Local.conf
Bitbake needs some basic configuration files in order to process a build, These files are *.conf
The minimally necessary ones as example files in the build/conf/local.conf
The local.conf file provides basic variables that define a build environment
  Target Machine : $MACHINE :
    Machine files includes settings about : target arch(x86,ARM) , bootloader,kernel,image type,compiler flags,soc configuration.
  Download Directory $DL_DIR
  Shared state directory $SSTATE_DIR
    cache mechanisam design to speed up the build process by reusing previous build component.
  Build Output $TMPDIR
  Distribution policy $DISTRO
  package management systems $PACKAGE_CLASSES
  specify additional features to include $EXTRA_IMAGE_FEATURES
  specify additional classes that should be applied $USER_CLASSES
  Monitor disk $BB_DISKMON_DIRS
  tracking changes $CONF_VERSION
  Show on terminal Add : BB_CHECK_SSL_CERTS = “0” ; need to add it because security issue in WWW.

## Slide 22: Build System concept

## Slide 23: Artifacts location
Default General location
<project_name>/build/tmp/deploy/images/<machine>/
Machine qemux86-64: show on terminal
/var/yocto/tmp/deploy/images/qemux86-64/
Xilinx-Mpsoc
<project_name>/build/tmp/deploy/images/zcu102-zynqmp/
Boot.scr , boot.bin , <image_name>-<machine_name>-<machine>

## Slide 24: Package Overview
refers to a recipes packaged output produced by Bitbake .
A package is generally the artifact binaries produced from the recipes sources .
There are 3 types of packages : rpm,deb,ipk :
  Rpm : widely used in various linux distribution which derived from Red Hat , Fedora and Centos
  Deb : used in Debian-based distribution like ubuntu
  Ipk: used by OpenEmbedded which closely related to Yocto.
  Configuration which type package to use selected in local.conf
Show on terminal
  Commands to find recipes to install packages:
    Bitbake-layers show-recipes bash
    Find the recipe : find . –name bash* (should find from ~/poky)
    Bitbake-layers show-recipes python3
    Bitbake-layers show-recipes git

## Slide 25: Package example
How to add packages to image
  There are few ways to do it :
    Local.conf to add IMAGE_INSTALL:append = “ <name_package/recipe>”
    Add it in poky image name we use for example “core-image-minimal”
    Use our own recipe we can create to build the image (will discuss later in images chapter)
Show on terminal
    Example how to install package with local.conf , later in images section we will implement it by image recipes.
    We can add the following line to add bash : IMAGE_INSTALL:append = “ bash” , save it.
    Test is by run emulator : runqemu slirp nographic (from separate terminal)

## Slide 26: Recipes - Overview
A set of instruction for building packages.
A recipe describes where you get source code , which patches to apply , from where to fetch packages , how to configure the source , how to compile it and so on.
A recipes describes dependencies for libraries or for other recipes .
A Recipes represent the logical unit of execution. The software to build , the images to build and use the .bb file extension.

## Slide 27: Recipes - example
Show on terminal how to use recipe to compile and build student app and use patch:
Steps:
  mkdir -p recipes-app/student-app/files
  Cp ../meta-skeleton/recipes-skeleton/hello-single/hello_1.0.bb recipes-app/student-app/student-app.bb
  cp ../meta-skeleton/recipes-skeleton/hello-single/files/helloworld.c recipes-app/student-app/files/
  Change the name build in .bb from ‘helloworld’ to ‘student-app’ .
  Build and run
  create patch :
    cd recipes-app/student-app/files/
    Copy the src file to other directory (files/tmp) and modify the print
    diff –u <first_file_src> <sec_file_src> ; note the files should be with same name – please make the second file under files/tmp for this.
    Add the patch file to recipe
  Build and run

## Slide 28: Recipe build task Overview and examples
List of all possible tasks: show on terminal
  Bitbake –c listtasks <recipe>
    Example Bitbake –c listtasks student-app
Each task we can use with the flag ‘-c’
Find tmp: bitbake –e student-app | grep ^S=
  Bitbake –c cleanall student-app
    Check log in tmp/temp/log.task_order
  Bitbake –c unpack student-app
    Check log in temp\log.task_order
  Bitbake –c compile student-app
    Check deploy file ‘student-app’ in tmp/
    one level less

## Slide 29: Recipe build task examples
  Bitbake –c install student-app
    Check log in temp\log.task_order

## Slide 30: Recipes build tasks function example
Do_configure – configures the source by enabling and disabling any build-time and configuration options for the software being built.
Do_compile – compiles the source in the compilation directory
Show live on terminal
Commands:
Show build task : bitbake –c listtasks <recipe_name>
Check Ovelayed : Bitbake-layers show-overlayed

## Slide 31: Recipes build tasks
Do_install – copies files and provide permissions from the compilation directory , which is defined by the ${WORKDIR}/${BP}/ to destination folder in ${WORKDIR}/image
Do_fetch – fetches the source code , this task uses the SRC_URI variable and the arguments prefix to determine the correct fetcher module . (default , not needed to implement )

## Slide 32: Recipes build tasks
do_patch : Locates patch files and applies them to the source code - usually not need to implement it .
Unpack (do_upack) : Unpacks the source code into a working directory – usually not need to implement it.

## Slide 33: Assignment
?= : This is used to assign the default value to variable. It can be overridden.
:= This is an immediate variable expansion. The value assigned is expanded immediately.
:append : This appends a value to a variable. The operator inserts no space between the current value and appended value. The effects are applied at variable expansion time rather than being immediately applied.
:prepend : similar to append – just the append is from the end to start
Example no space: A=“foo” , A:append = “bar” , A=“foobar”
Example with space : A=“foo” , A:append = “ bar” , A=“foo bar”
Example no space: A=“foo” , A:prepend = “bar” , A=“barfoo”
Example with space : A=“foo” , A:prepend = “ bar” , A=“bar foo”

## Slide 34: Basic Variables
FILESEXTRAPATHS_prepend : extend the search path the OpenEmbedded build system uses when looking for files and patches.
SRC_URI_append : the list of source files – local or remote .
IMAGE_INSTALL: used by recipe to specify the packages to install an image through the image class

## Slide 35: Basic Variables
${WORKDIR} : the pathname of the work directory.
The directory is located within the TMPDIR directory structure
  WORKDIR = ${TMPDIR}/work/${MULTIMACH_TARGET_SYS}/${PN}/${EXTENDPE}${PV}-${PR}
${TMPDIR} : the top level build output directory (build/tmp)
${MULTIMACH_TARGET_SYS} : the target system identifier .
${PN} : the recipe name ( package_name)
${PV} , ${PR} : recipe version ) package_version and revision)
Example : PN_PV_PR.bb example2_0.2_r0
S – Source
D – Destionion
B – Build directoty

## Slide 36: Basic Variables
Show on terminal for example on student-app recipe
  Read variable value syntax: Bitbake –e <recipe_name> | grep ^<Var_name>=
    Bitbake –e <recipe_name> | grep ^WORKDIR=
    Bitbake –e <recipe_name> | grep ^TOPDIR=
    Bitbake –e <recipe_name> | grep ^PN=
    Bitbake –e <recipe_name> | grep ^PV=
    Bitbake –e <recipe_name> | grep ^PR=
    Bitbake –e <recipe_name> | grep ^S=
    Bitbake –e <recipe_name> | grep ^D=
List of all the variable and documentation of Yocto here:
  Cat ~/poky/meta/conf/documentation.conf | grep <var_name>
  Firefox ./documentation/ref-manual/variables.rst
  12 Variables Glossary — The Yocto Project ® 5.0.999 documentation

## Slide 37: License
List of licences ./meta/files/common-licenses
Use license MIT
Calculate of checksum by : md5sum

## Slide 38: Append files - .bbappend
Files that append build information to a recipe file
Expected every append file to have a corresponding recipe .bb file. (this file should override)
The .bbappend file and .bb file should with the same name , for example : busybox_1.21.%.bbappend <-> busybox_1.21.1. bb
Information in append files extended or overrides the information in the similar-named recipe file.
The agenda is to use in .bb from other layer in other layer without to copy recipe and change it – layer agenda.

## Slide 39: Append files - busybox
Busybox is commonly used to provide a lighweight set of Unix utilities.
Link to busy box example configuration utilities (defconfig)
  poky/meta/recipes-core/busybox/busybox at master · CESARBR/poky (github.com)
Show on terminal how to modify busybox configuration by used of append files
  List of configuration : poky/meta-poky/recipes-core/busybox/busybox/poky-tiny/defconfig
  Mkdir <layer_name>/recipes-core
  Copy from poky/meta-skeleton/recipes-core/busybox to our layer <layer_name>/recipes-core
  Generate fragment by : bitbake busybox –c menuconfig ; bitbake busybox –c diffconfig
  Copy devmem fragment from generated location to YoctoStudent/recipes-core/busybox/busybox/
  Give meaning name = enable_devmem.cfg
  Add the fragment name file to the append file
  Bitbake busybox –c cleanall
  Build and run
Command display all the appends
  Bitbake-layers show-appends
  Show priority layer : bitbake-layers show-layers

## Slide 40: Image
An Image is an artifact of the BitBake build process given a collection of recipes and related metadata .
Images are the binary output that run on specific hardware or QEMU and are used for specific use-cases
You often need to create your own image recipe , in order to add new packages or functionally , rather than using the base images , which are provided by the base layers.
The simply way is to inherit image classes.
The output images located at : tmp/deploy/images/<machine_name>

## Slide 41: Image Inherit
Core-image-minimal.bb
Core-image.bbclass
Image.bbclass
Bitbake
Inherit process while we build the image flow
Show in terminal how to prepare modified image :
  Overview .bbclass image in poky : find . –name core-image*.bbclass – will discuss more in class section.
  Copy core-image-minimal.bb to our layer under /recipes-core/images
    Find . –name core-image-minimal.bb
    Mkdir –p <student_layer>/recipes-core/images
    Cp core-image-minimal.bb <student_layer>/recipes-core/images/student-minimal.bb
  Add packages in IMAGE_INSTALL:append = “ bash student-app”
  Remove from local.conf the “bash student-app”
  Build with our ‘student-minimal’ and run

## Slide 42: Classes - .bbclass
Class files are used to abstract common functionality and share it amongst multiple recipe (.bb) files .
To use a class file , need a recipe file that will inherits the relevant class
In most cases, when a recipe inherits a class it is enough to enable its features.
Examples of important classes files are used : image.bbclass, cmake.bbclass,kernel-fitimage.bbclass,autotools ,and many more..
Link for overview of classed : 5 Classes — The Yocto Project ® 5.0.3 documentation
bbclass files resident under classes folder

## Slide 43: Classes – practical
.
Assume we got a task to add user to our image addition to root :
Show on terminal:
Edit our image file as we do in previous image slide
Add the below content of file:
Inherit extrausers
Build student-image
Run emulator :
  Switch to user : su – student
  Check what currently user : whoami
  Check id user : id student
  Check group user : groups student

## Slide 44: Linux / U-boot Fragment – Method1
Demonstrate one of both in terminal:
Generate fragment Linux-kernel:
  Bitbake linux-yocto–c menuconfig
    Do your change , save and exit
  Bitbake linux-yocto –c diffconfig
    The bitbake will provide the location of generated fragment .cfg path – copy it
  Copy .cfg to temp and name it with meaning name
    Example : disable_bt.cfg
Generate fragment U-boot:
  Bitbake u-boot –c menuconfig
    Do your change , save and exit
  Bitbake u-boot –c diffconfig
    The bitbake will provide the location of generated fragment .cfg path – copy it
  Copy .cfg to temp and name it with meaning name
    Example : disable_spl.cfg

## Slide 45: Linux Configuration – method1
Prepare the recipe and bbappend Linux-kernel
  read kernel yocto version : bitbake –e linux-yocto| grep “^PV”
  Mkdir –p ~/poky/YoctoStudent/recipes-kernel/linux/linux-yocto
  Touch and Open for edit ~/YoctoStudent/recipes-kernel/linux/linux-yocto_%.bbappend
  Write the below template
    FILESEXTRAPATHS:prepend := “${THISDIR}/${PN}:”
    SRC_URI +=“file://<cfg_file_name> “
    Add your change .cfg file – for example disable_bt.cfg
  Copy fragment file to ~/YoctoStudent/recipes-kernel/linux/linux-yocto
  Build image

## Slide 46: U-boot Configuration – method1
Prepare the recipe and bbappend U-boot
Check u-boot yocto version : bitbake –e virtual/bootloader | grep “^PV”
  Mkdir –p ~/YoctoStudent/recipes-bsp/u-boot/u-boot
  Touch and Open for edit ~/YoctoStudent/recipes-bsp/u-boot/u-boot_%.bbappend
  Write the below template
    FILESEXTRAPATHS:prepend := “${THISDIR}/${PN}:”
    SRC_URI +=“file://<cfg_file_name> “
    Add your change .cfg file – for example disable_bt.cfg
  Copy fragment file to ~/YoctoStudent/recipes-bsp/u-boot/u-boot/
  Build image

## Slide 47: Linux / Uboot Configuration – method2
Use devtool for Linux-kernel
  devtool modify linux-yocto - gernearte workspace for modify kernel
  Devtool menuconfig linux-yocto – will open the menu
  Change and save – will provide .cfg to workspace
  Devtool finish linux-yocto - will provide bbappend with the change that will include the fragment file
Use devtool for U-boot
  devtool modify u-boot - gernearte workspace for modify u-boot
  Devtool menuconfig u-boot – will open the menu
  Change and save – will provide .cfg to workspace
  Devtool finish u-boot - will provide bbappend with the change that will include the fragment file

## Slide 48: SDK - Toolchain
Disable ssl certificate (avoid Rafael WWW block)
  Build/conf/local.conf
  Add : BB_CHECK_SSL_CERTS = “0”
  Save and exit
Run from build directory : bitbake <image> -c populate_sdk (please note this operation can take 1 hour and size addition of ~60G).
Cd /var/yocto/tmp/deploy/sdk
Run the bash install script that located in this directory .(.sh)
Go to path which you deploy the sdk in the installation.
Run : source envoirment-setup-<machine_name_arch>-<distro>-linux
  Example: source envoirment-setup-core2-64-poky-linux
After source you can find the gcc / g++ according to machine arch , for example in case of x86_64 : x86_64-linux-gnu-gcc
Example : x86_64-linux-gnu-gcc main.c –o hellow

## Slide 49: Practice

## Slide 50: Practice
Exercise1:
  create and add new layer to your project – name it ‘meta-student’ – verify that layer added .
  Copy file core-image-minimal.bb (use find command ) to your recipe core inside your layer (recipes-core/images/) , name it student-image.bb
  Build the image with this recipe
  Run runqemu slirp nographic (from separate terminal)

## Slide 51: Practice
Exercise2:
  Create a new toolchain for your project (use sdk slide)
    Please note this operation can take ~1 hour and addition size of 60 G
  Edit simple hellow-world.c that do some print to screen and save
  Compile it use your cross-compiler sdk (gcc-*) – follow the sdk slide .
  Verify you have executable file .

## Slide 52: Practice
Exercise3:
  Step1:
    Add new recipe inside the layer from ex1 , call it recipe-<name_app> that implement the below :
      Compile the file
      Install the file to /usr/bin
    Install the application to the image – in the image you create in ex1
    Build and run the emulator
    Check that you can run the application in the target
    Hint : check ‘meta-skeleton’ for template.
  Step2:
    Add new recipe that called ‘recipe-init’
      In this task need to use sysvinit init-manager , follow the below:
        Create .bb file that add an init script to your image
        The init script will run the app from ex1 and direct log as follow name_app > /tmp/log.txt
        Hint : use template file recipes-init that copied to docker in /var/yocto/practice/recipes-init
    Build and run the emulator
    Print the log : cat /tmp/log.txt

## Slide 53: Practice
Exercise4:
  Step1:
    Create bbclass and call it debug_tools
    Write inside it all the debug tools you want to it : stress-ng, valgrind
  Step2:
    Add to your custom image the debug_tools by use inherit
    Build and run
    Check that you have these tools in your image

## Slide 54: Practice
Exercise5:
  Step1:
    Change the recipe-init script that the application will direct the print to /dev/kmsg – kernel log
    Build and run
    Note that you should see the print of the app to the screen and not just the log ? Why?
  Step2:
    Configure the kernel following the below , you can use 2 methods : devtool or create fragment and manually add it to bbappend.
    Disable the print of the kernel log to the screen by configuration of the log level in kernel configuration.
    Search for variable CONSOLE_LOGLEVEL_DEFAULTS
    Build and run
    Hint : use template file recipes-kernel that copied to docker : /var/yocto/practice/recipes-init

## Slide 55: Linux Commands
Search text into folders and directories
  Find –type f –exec grep –lr “text” {} \;
Search file name
  Find . –name <name>

## Slide 56: Yocto with Xilinx BSP layers

## Slide 57: Xilinx Layers
Yocto-poky – layers default:
  Link : yoctoproject/poky at honister (github.com)
meta-xilinx:
  Link : Xilinx/meta-xilinx at honister (github.com)
  Add layers : meta-Xilinx-core , meta-Xilinx-bsp (require meta-oe) , meta-Xilinx-standalone
  Readme : meta-Xilinx-core
meta-oe:
  Link : openembedded/meta-openembedded at honister (github.com)
  Add layer : meta-oe
Meta-xilinx-tools:
  Link : Xilinx/meta-xilinx-tools at honister (github.com)
  Add layers : meta-Xilinx-tools (require meta-oe,meta-Xilinx-standalone,meta-poky)
  ReadMe : meta-Xilinx-tools – see HW config with XSA.

## Slide 58: Yocto with Xilinx Configuration
Packages to install:
  Yocto Project Quick Build — The Yocto Project ® 3.4.999 documentation
Local.conf (edit override machine file according to slide 67)
  MACHINE= “ zcu102-zynqmp-rf”
bblayer.conf
  <project_dir>/meta-openembedded/meta-oe
  <project_dir>/meta-Xilinx/meta-xilinx-bsp
  <project_dir>/meta-Xilinx/meta-xilinx-core
  <project_dir>/meta-Xilinx/meta-xilinx-standalone
  <project_dir>/meta-Xilinx-tools

## Slide 59: Xilinx Configuration
Create own layer or add it to distro the below configuration:
Config image as initramfs:
  IMAGE_FSTYPES:remove = “wic.qemu-sd”
  INITRAMFS_IMAGE = “core-image-minimal”
enable generated boot script
  EXTRA_IMAGEDEPENDS:Append = “ u-boot-zynq-scr”
Config image as FIT image
  KERNEL_CLASSES += “kernel-fitimage”
  KERNEL_IMAGETYPES:append = “ fitImage”
  UBOOT_ENTRYPOINT_zynqmp = “0x80000”
  UBOOT_LOADADDRESS_zynqmp = “0x80000”
Hardware Description (XSA)
  HDF_BASE= “file://”
  HDF_PATH = "/<absolute-path-to-xsa>/system.xsa"

## Slide 60: Xilinx Configuration
Hardware Description (XSA) - continue
  Link to XSA files : hdf-examples/ at rel-v2020.1 · Xilinx/hdf-examples (github.com)
LICENSE
  Add this line to your project layer : LICENSE_FLAGS_WHITELIST += “Xilinx”
Config Device tree
  Add configuration for your custom device-tree according link below
    Customizing Device Trees in Xilinx Yocto - Xilinx Wiki - Confluence (atlassian.net)
  Set the variable SYSTEM_USER_DTSI to the full path to your system-user.dtsi file
  Create file system-user.dtsi in the location you create
  In order to see the source device tree and psu files , should run : bitbake device-tree –c compile –f
  You can find the sources : build/tmp/work/<image_linux_name>/device-tree/xilinx-…./device-tree-build/device-tree/
  Example :

## Slide 61: Xilinx Configuration - Machine
Add override for your selected machine – example zcu102:
Under your project layer:
  <project_name>/conf/machine/zcu102-zynqmp-rf.conf
Add the below content:
  require conf/machine/zcu102-zynqmp.conf
  MACHINEOVERRIDES =. “zcu102-zynqmp:”
  UBOOT_ENTRYPOINT = “0x80000”
  UBOOT_LOADADDRESS = “${UBOOT_ENTRYPOINT}”

## Slide 62: Artifact – Xilinx
Path to Artifact:
  Build/tmp/deploy/images/<name_machine>/
Important basic Deploy Files
  Boot.bin
  Boot.scr
  fitImage-<image_name>-<machine_name>-<machine_name>

## Slide 63: Commands yocto relate to xilinx
Config kernel:
  Bitbake linux-xlnx –c menuconfig
  Bitbake linux-xlnx –c diffconfig
Config U-boot:
  Bitbake u-boot-xlnx –c menuconfig
  Bitbake u-boot-xlnx –c diffconfig
Fsbl (PATCHS)
  Generally need to add fsbl directory in your project : <my_project>/recipes-bsp/fsbl/files
  In <my_project>/recipes-bsp/fsbl/fsbl_%.bbappend
  Write the below :
    FILESEXTRAPATCHS:prepend := “${THISDIR}/files”
    SRC_URI:append = “file://file.patch”

## Slide 64: Appendix Rafael shield distro

## Slide 65: Layers Overview
There are 3 important layers in the build structure
Poky Yocto reference layer - distro .
Shield distro layer - our customized distro
  this layer is used poky distro and do some addition customization for this layer .
Project Layer - customized layer per project
  This layer is used specific per project , this is the most high level layer that provided specific with project , it include select machine target,xsa file , device-tree, fsbl specific or uboot configuration ,linux packages specific , modules , drivers , app and so on.
Meta -POKY
Shield-distro
Project layer

## Slide 66: Distro Layer - Overview
Distribution: specific implementation of linux (kernel version,rootfs,etc)
The distribution layer provides policy configuration for your distribution.
Best practice that you isolate these types of configuration into their own layer.
Settings you provide in conf/distro/distro.conf
In distribution layer usually you will find:
  Classes – hold common functionality that can be shared among recipes in the distribution
  Conf – hold configuration files for the layer
  Recipes – recipes and append files that affect common functionality

## Slide 67: Inherit image flow and structure
-inherit Core-image - inherit shield-users
inherit
Shield-image
inherit shield-image-initramfs
ext/rafael/meta-shield/classes/shield-image.bbclass
inherit image
./core/poky/meta/classes/core-image.bbclass
image
./core/poky/meta/classes/image.bbclass
meta-project-cxy/recipes-core/images/cxy-image-minimal.bb
ext/rafael/meta-shield/classes/shield-image-initramfs.bbclass
POKY-meta-distro
Meta-shield-distro
Meta-project-layer
Class poky
Class shield
Recipe bitbake : bitbake cxy-image-minimal

## Slide 68: project Layer structure
Bsp – include device-tree , XSA files per target
Conf – configuration per project
Machine – include machine file per project
Recipes bsp : include u-boot,fsbl,pmu,etc..
Recipes-core : include base files , scripts run and ability to add files to rootfs , can used to configure add permission , add aliases and more .
Images – should contain the recipre name to build the image specific for projects
Can contain application source
Can contain drivers and modules .
Can contain kernel specific configuration.
Configure the network and IP’s

## Slide 69: BSP layer / recipes - Overview
Machine: defines the architecture, pins, buses , BSP etc.
  The BSP layer provides machine configuration that target specific hardware.
  All in this layer is specific to the machine for which you can building the image
  The BSP layer configuration directory configuration files for the machine – conf/machine/machine.conf
FSBL – implements patches on source file , settings
UBOOT - implements patches on source file , configuration
SENSORS
MULITMEDIA
PMU
FPGA
BITSTREAM
ETC..

## Slide 70: BSP – machine structure
From project bsp layer :meta-project-cxy/conf/machine/zcu102-zynqmp-rf.conf
From Xilinx bsp layer : /xilinx/meta-xilinx/meta-xilinx-bsp/conf/machine/zcu102-zynqmp.conf
In local.conf :

## Slide 71: Rafael layers packages
meta-dss – This layer contains target tool.
Meta-fsb – new generation driver (high speed technology network)
Meta-gigevision – is a communication standart designed for industrial cameras used in machine vision and imaging applications.
Meta-htp - scripts required by Rafael's HTP target program. Used for testing the board
meta-linux-debug-settings - A layer that allows to easily enable many useful linux debug settings
meta-linux-drivers - A layer for various Linux drivers
meta-linux-libs - A layer that contains various libs for Linux.
meta-linux-utils - general Linux utilities
meta-openrc-ext - An extension to meta-openrc layer
meta-process-isolation - This layer provides process isolation functionalty based on NsJail utility.
meta-realtime-kernel - RT patch + relevant kernel configuration for real-time scheduling.
meta-xilinx-wrapper - A wrapper over Xilinx layers