## Slide 1: Yocto Tutorial Beginner
Yaron Daniel

## Slide 2: Syllabus
Introduction
  Embedded system
  Embedded Linux
  Linux distribution build platforms
  Petalinux compare Yocto
  OpenEmbedded and Yocto
Yocto
    Install and Build image
    Bitbake
    Poky
    Layers
    Bblayers.conf
    Local.conf
    Build system
    Artifacts
    Packages
    Recipes
    Recipes build task
    Basic assignment
    Variables

## Slide 3: Syllabus - continue
  Yocto
    Bbappend
    images
    Classes
    Kernel configuration
    Uboot configuration
  Appendix – Rafael shield distro
  Practice

## Slide 4: Embedded Systems - Overview
Embedded system is a combination of a computer hardware and software designed for a specific function
The systems can be programmable or have a fixed functionality
Example include :
  Automotive : modern cars commonly consist of many computers ,design to perform different tasks within vehicle . Such as adaptive cruise control ,forward collision warning , navigation system etc..
  Mobiles phones : these consist of many embedded systems including GUI software and hardware , operating systems , cameras , microphone etc..
  Industrial machines : sensors , automation system that perform specific monitoring and control function .
  Medical equipment : sensors , control mechanism , complex OS for GUI , CT scan , X-ray , MRI , etc..

## Slide 5: Embedded Systems – Characteristics
Consist hardware , software and firmware
  Basic Hardware : processor, power supply, memory, flash,communication port.
  Firmware : implement of FPGA
  Software : embedded OS , application task.
Can be embedded in a large system to perform a specific function , as they are built for specialized task within the system.
Can be microprocessor or microcontroller and compute power.
Real time : require to perform their function under a time constraint to keep the larger system functioning properly (usually baremetal , linux by default is not real-time.)

## Slide 6: Embedded Linux - Overview
Embedded linux refers to the use of the Linux Kernel , along with a comprehensive set of libraries and utilities, within embedded system or devices.
These systems, which are designed for specific functions, often feature constraints on resource like processing power, memory and energy consumption.
Linux due to its open-source nature, flexibility and robustness has become a popular choice for these systems.

## Slide 7: Embedded Linux
A linux distribution or distro is an operating system made up of the linux kernel along with a package management system and various libraries , drivers and utilities .
In the context of the Embedded linux, a distribution is often stripped down and customized to fit the needs of the specific embedded system it’s intended to run on.
There are several linux distribution platform specifically designed for embedded systems, such as OpenWrt, Yocto and buildroot.

## Slide 8: Linux distribution platforms
Buildroot : Based on set of Makefiles and patches that simplifies and automates the process of building a complete and bootable linux environment while using cross-compilation to allow building for multiple target platforms on a single linux based development system.
  Easy to use
  Limited configuration settings
  Requires full image rebuild
OpenWrt : Is an open-source project for embedded based on linux , used on embedded devices to route network traffic . All the components have been optimized to be small enough to fit into the limited storage and memory available in home routers.
  Focused on networking gear (routers)
  Packages based updated
Yocto : Yocto project is an open source project imitated by linux foundation . It provide a set of tools and metadata that enable developers to build custom linux distributions for embedded systems.
PetaLinux : Is a development enviorment by Xilinx , a leading provider of FPGA and SOC solution . It designed to streamline the development process for embedded linux system on Xilinx devices . MPSOC and Zynq SOC.

## Slide 9: PetaLinux compare Yocto Overview
PetaLinux Advantages
  Specialized for Xilinx hardware – specifically tailored for Xilinx FPGA and SOC
  Streamlined workflow – more integrated and streamlined for Xilinx development to Yocto – can reduce development time.
  Xilinx support
  Pre-built components – configuration optimized for Xilinx devices.
PetaLinux disadvantages
  Vendor Xilinx – lock – not intended for other targets
  Limited flexibility – lack of the flexibility and customization options provided by Yocto
  Dependency on Xilinx tools – heavily relies on Xilinx development tools which can introduce dependencies and constraints in the development process .

## Slide 10: PetaLinux compare Yocto Overview
Yocto Advantages
  Platform independence – Yocto project can be used to build custom linux for a wide range of embedded .
  Highly customization – Yocto offers extensive flexibility and customization options through its layer based architecture , allowing developers to tailor linux distribution to specific reequipment .
  Large community support.
Yocto disadvantages
  Learning curve – Yocto project has a steep learning curve , especially for beginner due to its complexity and extensive feature set. Getting started and mastering the workflow may require time and effort.
  Configuration overhead – Yocto require more configuration and setup compared to petalinux. (can be less if we used Xilinx layers for Yocto)
  Potential integration failures.
Summary: the choice between Petalinux and Yocto project depending on factors of hardware (Xilinx or not) , development preferences , customizations needs and resources (time) .

## Slide 11: OpenEmbedded and Yocto
OpenEmbedded is the underlying build framework , while Yocto project builds upon it to provide a comprehensive set of tools , documents,and best practices for embedded linux development .
Developers often use the Yocto project to create custom linux distro for their embedded systems , leveraging both OpenEmbedded capabilities and additional features provide Yocto.

## Slide 12: Yocto

## Slide 13
TODO - WIP
Instruction how to access Docker Image to build for the practice

## Slide 14
Install and build image
Download page:
- https://docs.yoctoproject.org/4.0.18/brief-yoctoprojectqs/index.html (kirksotne version)
- Include step by step install and system requirement according to branch version .
Releases tables: https://wiki.yoctoproject.org/wiki/Releases
Include data for supported versions and status
Notes: 14

## Slide 15: Install and build image
Steps:
sudo mkdir -p /YoctoStudent
Sudo chown -R ubuntu /YoctoStudent
cd /YoctoStudent
Install Packages:
  sudo apt install gawk wget git diffstat unzip texinfo gcc build-essential chrpath socat cpio python3 python3-pip python3-pexpect xz-utils debianutils iputils-ping python3-git python3-jinja2 libegl1-mesa libsdl1.2-dev python3-subunit mesa-common-dev zstd liblz4-tool file locales
sudo locale-gen en_US.UTF-8
git clone git://git.yoctoproject.org/poky
cd poky
git checkout -t origin/kirkstone -b my-kirkstone
. oe-init-build-env
export LC_ALL=C # for every terminal add this line to ~/.bashrc
bitbake core-image-minimal
Show on terminal (without run bitbake build – just check that bitbake is working)

## Slide 16: Bitbake
The task executor and scheduler used by the OpenEmbedded build system to build images.
It reads metadata and executes tasks defined in those files to build software packages and create images.

## Slide 17: Poky - Overview
Reference embedded distribution and a reference test configuration.
Poky provide the following :
  A base-level functional distro used to illustrate to customize a distribution.
  A means by which to test the Yocto components
  Download the Yocto : Bitbake , OpenEmbedded-core,documentation and source of information.
  Show on terminal poky structure :
  poky: Poky is a reference distribution of the Yocto Project®.

## Slide 18: User Configuration – Scheme

## Slide 19: Layer Overview
A collection of related recipes . (such as graphic,multimedia,etc..)
Layer allow you to consolidate relate metadata to customize your build. (debug,oper,..etc)
Layer allow isolate information used when building for multiple architectures (projects).
Layer are hierarchical in their ability to override previous specifications.(bbappend,inherit bbclass)
You can include any number of available layers from the Yocto project and customize the build by add our layers (configure conf file,machine,device-tree ,etc..)
In this tutorial we will demonstrate and build our own layer.

## Slide 20: Layer - bblayers.conf
bblayers.conf is a configuration file used by the build system.
In this file the set of layers are defined ,should be included in a build.
The bblayers.conf file specifies the location of each layer on the local file system.
Show on terminal
  Show layers: bitbake-layers show-layers (should run from build folder)

## Slide 21: Layers practical
Show on terminal commands:
  Help : bitbake-layers –h
  Show layers : bitbake-layers show-layers
  Create layer : bitbake-layers create-layer <path/to/layer>
  Add layer : bitbake-layers add-layer <path/to/layer>
Example:
  Bitbake-layers create-layer ~/YoctoStudent
  Bitbake-layers add-layer ~/YoctoStudent (from build dir)

## Slide 22: User Configuration Local.conf
Bitbake needs some basic configuration files in order to process a build, These files are *.conf
The minimally necessary ones as example files in the build/conf
The local.conf file provides basic variables that define a build enviorment
  Target Machine : $MACHINE
  Download Directory $DL_DIR
  Shared state directory $SSTATE_DIR
  Build Output $TMPDIR
  Distribution policy $DISTRO
  package management systems $PACKAGE_CLASSES
  specify additional features to include $EXTRA_IMAGE_FEATURES
  specify additional classes that should be applied $USER_CLASSES
  Monitor disk $BB_DISKMON_DIRS
  tracking changes $CONF_VERSION
  Show on terminal – present the local.conf

## Slide 23: Build System concept

## Slide 24: Artifacts location
Default General location
<project_name>/build/tmp/deploy/images/<machine>/
Machine qemux86-64:
/var/yocto/tmp/deploy/images/qemux86-64/
Xilinx-Mpsoc
<project_name>/build/tmp/deploy/images/zcu102-zynqmp/
Boot.scr , boot.bin , <image_name>-<machine_name>-<machine>

## Slide 25: Package Overview
refers to a recipes packaged output produced by Bitbake .
A package is generally the artifact binaries produced from the recipes sources .
There are 3 types of packages : rpm,deb,ipk :
  Rpm : widely used in various linux distribution which derived from Red Hat , Fedora and Centos
  Deb : used in Debian-based distribution like ubuntu
  Ipk: used by OpenEmbedded which closely related to Yocto.
  Configuration which type package to use selected in local.conf
Show on terminal
  Commands to find recipes to install packages:
    Bitbake-layers show-recipes | grep bash
    Find the recipe : find . –name bash* (should find from ~/poky)
    Bitbake-layers show-recipes python3
    Bitbake-layers show-recipes git

## Slide 26: Package example
How to add packages to image
  There are few ways to do it :
    Local.conf to add IMAGE_INSTALL:append = “ <name_package/recipe>”
    Add it in poky image name we use for example “core-image-minimal”
    Use our own recipe we can create to build the image (will discuss later in images chapter)
Show on terminal
    Example how to install package with local.conf , later in images section we will implement it by image recipes.
    We can add the following line to add bash : IMAGE_INSTALL:append = “ bash” , save it.
    Test is by run emulator : runqemu slirp nographic (from separate terminal)

## Slide 27: Recipes - Overview
A set of instruction for building packages.
A recipe describes where you get source code , which patches to apply , from where to fetch packages , how to configure the source , how to compile it and so on.
A recipes describes dependencies for libraries or for other recipes .
A Recipes represent the logical unit of execution. The software to build , the images to build and use the .bb file extension.

## Slide 28: Recipes - example
Show on terminal how to use recipe to compile and build student app and use patch:
Steps:
  Create dir for meta-student/recipe app/student-apps/files
  Cp sample-example.bb to /student-apps/student-apps.bb
  Cp hellow-student.c to /files
  Cp 0001-hellow-modify.patch to /files
  Edit the recipe file and add both files
  Edit do_compile function
  Build and run – check if patch effect on changed ?

## Slide 29: Recipe build task Overview and examples
List of all possible tasks:
  Bitbake –c listtasks <recipe>
    Example Bitbake –c listtasks student-app
Each task we can use with the flag ‘-c’
  Bitbake –c cleanall student-app
    Check : bitbake –e student-app | grep ^S=
    Check log in temp\log.task_order
  Bitbake –c unpack student-app
    Check : bitbake –e student-app | grep ^S=
    Check log in temp\log.task_order
  Bitbake –c compile student-app
    Check bitbake –e student-app | grep ^S=
    Check file student-app (artifact)

## Slide 30: Recipe build task examples
  Bitbake –c install student-app
    Check bitbake –e student-app | grep ^S=
    Check images folder (artifact)

## Slide 31: Recipes build tasks function example
Do_configure – configures the source by enabling and disabling any build-time and configuration options for the software being built.
Do_compile – compiles the source in the compilation directory
Show live on terminal
Commands:
Show build task : bitbake –c listtasks <recipe_name>
Check Ovelayed : Bitbake-layers show-overlayed

## Slide 32: Recipes build tasks
Do_install – copies files and provide permissions from the compilation directory , which is defined by the ${WORKDIR}/${BP}/ to destination folder in ${WORKDIR}/image
Do_fetch – fetches the source code , this task uses the SRC_URI variable and the arguments prefix to determine the correct fetcher module . (default , not needed to implement )

## Slide 33: Recipes build tasks
do_patch : Locates patch files and applies them to the source code - usually not need to implement it .
Unpack (do_upack) : Unpacks the source code into a working directory – usually not need to implement it.

## Slide 34: Assignment
?= : This is used to assign the default value to variable. It can be overridden.
:= This is an immediate variable expansion. The value assigned is expanded immediately.
:append : This appends a value to a variable. The operator inserts no space between the current value and appended value. The effects are applied at variable expansion time rather than being immediately applied.

## Slide 35: Basic Variables
FILESEXTRAPATHS_prepend : extend the search path the OpenEmbedded build system uses when looking for files and patches.
SRC_URI_append : the list of source files – local or remote . This variable tells bitbake which bits to pull for the build and how to pull them.
IMAGE_INSTALL: used by recipe to specify the packages to install an image through the image class

## Slide 36: Basic Variables
${WORKDIR} : the pathname of the work directory.
The directory is located within the TMPDIR directory structure
  WORKDIR = ${TMPDIR}/work/${MULTIMACH_TARGET_SYS}/${PN}/${EXTENDPE}${PV}-${PR}
${TMPDIR} : the top level build output directory (build/tmp)
${MULTIMACH_TARGET_SYS} : the target system identifier .
${PN} : the recipe name ( package_name)
${PV} , ${PR} : recipe version ) package_version and revision)
Example : PN_PV_PR.bb example2_0.2_r0
S – Source
D – Destionion
B – Build directoty

## Slide 37: Basic Variables
Show on terminal for example on student-app recipe
  Read variable value syntax: Bitbake –e <recipe_name> | grep ^<Var_name>=
    Bitbake –e <recipe_name> | grep ^WORKDIR=
    Bitbake –e <recipe_name> | grep ^TOPDIR=
    Bitbake –e <recipe_name> | grep ^PN=
    Bitbake –e <recipe_name> | grep ^PV=
    Bitbake –e <recipe_name> | grep ^PR=
    Bitbake –e <recipe_name> | grep ^S=
    Bitbake –e <recipe_name> | grep ^D=

## Slide 38: Append files - .bbappend
Files that append build information to a recipe file
Expected every append file to have a corresponding recipe .bb file. (this file should override)
The .bbappend file and .bb file should with the same root name , for example : busybox_1.21.%.bbappend <-> busybox_1.21.1. bb
Information in append files extended or overrides the information in the similary-named recipe file.
The agenda is to use in .bb from other layer in other layer without to copy recipe and change it – layer agenda.

## Slide 39: Append files - busybox
Busybox is commonly used to provide a lighweight set of Unix utilities.
Link to busy box example configuration utilities
  poky/meta/recipes-core/busybox/busybox at master · CESARBR/poky (github.com)
Show on terminal how to modify busybox configuration by used of append files
  List of configuration : poky/meta-poky/recipes-core/busybox/busybox/poky-tiny/defconfig
  Copy from poky/meta-skeleton/recipes-core/busybox to our layer meta-student/recipes-core
  Copy devmem configuration from defconfig and create fragment in the busybox/busybox folder . (CONFIG_DEVMEM=y) enable_devmem.cfg
  Add the fragment name file to append file
Command display all the appends
  Bitbake-layers show-appends
  Show priority layer : bitbake-layers show-layers

## Slide 40: Image
An Image is an artifact of the BitBake build process given a collection of recipes and related metadata .
Images are the binary output that run on specific hardware or QEMU and are used for specific use-cases
You often need to create your own image recipe , in order to add new packages or functionally , rather than using the base images , which are provided by the base layers.
The simply way is to inherit image classes.
The output images located at : tmp/deploy/images/machine

## Slide 41: Image Inherit
Core-image-minimal.bb
Core-image.bbclass
Image.bbclass
Bitbake
Inherit process while we build the image flow
Show in terminal how to prepare modified image :
  Overview .bbclass image in poky : find . –name core-image*.bbclass – will discuss more in class section.
  Copy core-image-minimal.bb to our layer under /recipes-core/images
  Add packages in IMAGE_INSTALL:append = “ bash”
  In next chapter we will use in class.

## Slide 42: Classes - .bbclass
Files that provide for logic encapsulation and inheritance so that commonly used patterns can be defined once and then easily used in multiple recipes
To use a class file , need that recipe file will inherits the relevant class or class can also inherit other class
bbclass and are usually placed in a classes/

## Slide 43: Classes – practical
.
Assume we got a task to add user to our image addition to root :
Show on terminal:
Edit our core-image-minimal-student.bb from image slide
Add the below content of file:
Inherit extrausers
EXTRA_USERS_PARAMS = “\
useradd –p ‘’ student; \
groupadd student-group; \
usermod –a –G student-group student; \
“
Build core-image-minimal-student
Run emulator :
  Switch to user : su – student
  Check what currently user : whoami
  Check id user : id student
  Check group user : groups student

## Slide 44: Kernel linux Configuration
Generate fragment:
  Bitbake virtual/kernel –c menuconfig
    Do your change , save and exit
  Bitbake virtual/kernel –c diffconfig
    The bitbake will show the .cfg path – copy it
  Copy .cfg to temp and name it
    Example : disable_bt.cfg

## Slide 45: Kernel linux Configuration
Prepare the recipe and bbappend
  Check kernel yocto version : bitbake –e virtual/kernel | grep “^PV”
  In poky run : find . –name linux* | grep <PV>
  Mkdir ~/YoctoStudent/recipes-kernel/linux/linux
  Copy bbappend from find to ~/YoctoStudent/recipes-kernel/linux/
  Open for edit ~/YoctoStudent/recipes-kernel/linux/bbappend
  Delete all the content
  Write the below template
    FILESEXTRAPATHS_prepend := “${THISDIR}/${PN}:”
    SRC_URI +=file://
    Add your change .cfg file – for example disable_bt.cfg
  Copy from /tmp/disable_bt.cfg file to ~/YoctoStudent/recipes-kernel/linux/linux-yocto

## Slide 46: Xilinx

## Slide 47: Xilinx Layers Machine
Meta-Xilinx layers : Xilinx/meta-xilinx at kirkstone-next (github.com)
Meta-Xilinx-tools : Xilinx/meta-xilinx-tools: Yocto Project layer enables AMD Xilinx tools related metadata for MicroBlaze, Zynq, ZynqMP and Versal devices. (github.com)
local.conf
MACHINE = "zcu102-zynqmp“
HDF_MACHINE = "zcu102-zynqmp“
Device tree
  YAML_DT_BOARD_FLAGS = "{BOARD zcu102-rev1.0}“
IMAGE_FSTYPES += "wic“
WKS_FILES = "xilinx-default-sd.wks“
XSA
  HDF_BASE = file://
  HDF_PATH = "/home/student/poky/xsa“
  HDF_NAME = "cxy.xsa"

## Slide 48: Appendix Rafael shield distro

## Slide 49: Layers Overview
There are 3 important layers in the build structure
Poky Yocto reference layer - distro .
Shield distro layer - our customized distro
  this layer is used poky distro and do some addition customization for this layer .
Project Layer - customized layer per project
  This layer is used specific per project , this is the most high level layer that provided specific with project , it include select machine target,xsa file , device-tree, fsbl specific or uboot configuration ,linux packages specific , modules , drivers , app and so on.
Meta -POKY
Shield-distro
Project layer

## Slide 50: Distro Layer - Overview
Distribution: specific implementation of linux (kernel version,rootfs,etc)
The distribution layer provides policy configuration for your distribution.
Best practice that you isolate these types of configuration into their own layer.
Settings you provide in conf/distro/distro.conf
In distribution layer usually you will find:
  Classes – hold common functionality that can be shared among recipes in the distribution
  Conf – hold configuration files for the layer
  Recipes – recipes and append files that affect common functionality

## Slide 51: Inherit image flow and structure
-inherit Core-image - inherit shield-users
inherit
Shield-image
inherit shield-image-initramfs
ext/rafael/meta-shield/classes/shield-image.bbclass
inherit image
./core/poky/meta/classes/core-image.bbclass
image
./core/poky/meta/classes/image.bbclass
meta-project-cxy/recipes-core/images/cxy-image-minimal.bb
ext/rafael/meta-shield/classes/shield-image-initramfs.bbclass
POKY-meta-distro
Meta-shield-distro
Meta-project-layer
Class poky
Class shield
Recipe bitbake : bitbake cxy-image-minimal

## Slide 52: project Layer structure
Bsp – include device-tree , XSA files per target
Conf – configuration per project
Machine – include machine file per project
Recipes bsp : include u-boot,fsbl,pmu,etc..
Recipes-core : include base files , scripts run and ability to add files to rootfs , can used to configure add permission , add aliases and more .
Images – should contain the recipre name to build the image specific for projects
Can contain application source
Can contain drivers and modules .
Can contain kernel specific configuration.
Configure the network and IP’s

## Slide 53: BSP layer / recipes - Overview
Machine: defines the architecture, pins, buses , BSP etc.
  The BSP layer provides machine configuration that target specific hardware.
  All in this layer is specific to the machine for which you can building the image
  The BSP layer configuration directory configuration files for the machine – conf/machine/machine.conf
FSBL – implements patches on source file , settings
UBOOT - implements patches on source file , configuration
SENSORS
MULITMEDIA
PMU
FPGA
BITSTREAM
ETC..

## Slide 54: BSP – machine structure
From project bsp layer :meta-project-cxy/conf/machine/zcu102-zynqmp-rf.conf
From Xilinx bsp layer : /xilinx/meta-xilinx/meta-xilinx-bsp/conf/machine/zcu102-zynqmp.conf
In local.conf :

## Slide 55: Rafael layers packages
meta-dss – This layer contains target tool.
Meta-fsb – new generation driver (high speed technology network)
Meta-gigevision – is a communication standart designed for industrial cameras used in machine vision and imaging applications.
Meta-htp - scripts required by Rafael's HTP target program. Used for testing the board
meta-linux-debug-settings - A layer that allows to easily enable many useful linux debug settings
meta-linux-drivers - A layer for various Linux drivers
meta-linux-libs - A layer that contains various libs for Linux.
meta-linux-utils - general Linux utilities
meta-openrc-ext - An extension to meta-openrc layer
meta-process-isolation - This layer provides process isolation functionalty based on NsJail utility.
meta-realtime-kernel - RT patch + relevant kernel configuration for real-time scheduling.
meta-xilinx-wrapper - A wrapper over Xilinx layers providing Petalinux look & feel